## Slide 1: SESSION 2
Variables & Loops

## Slide 2
SESSION 2
Vriables & Loops
The aim of this session is discovery the loops and conditional structures, the base of programming. In this session, the goal of the students is to understand how the the loops works and do programs. This session needs a scotch tape to create a line on the ground and obstacles (maybe pencil box…) Note : if ultrasonic dosn’t work, it can be possible that the robot have a batterie charge problem.
Teacher info :

## Slide 3: Quiz!
SESSION 2
Vriables & Loops
1) What are the 2 parts of a robot ? a) Material & Code b) Hardware & Software c) Electronics & Mechanics 2) What is an IDE ? a) A platform to code b) The code design c) The block code of Maqueen + 3) How does a motor convert ? a) Electricity in rotation b) Electricity in mechanics c) Electricity in sound
4) How to move the robot forward for 1 seconds ? a) b) c) 5) Is it possible to change the color of the LEDs ? a) Yes b) No 6) What parameters cannot be changed using a "music" block ? a) Intensity and tone b) Volume and melody name c) Melody and rhythm

## Slide 4: Summary
SESSION 2
Vriables & Loops
I/- The variables 1) What are variables ? 2) Create a variable 3) Exercise II/- Loops 1) What are loops ?
2) While loop
3) For loop
4) If-Else structure
III/- Sensors
1) Ultrasonic sensor 2) Line sensors
IV/- The mission 1) Explanations 2) Challenge
V/- Additional Time

## Slide 5: I/- Variables
SESSION 2
Vriables & Loops
A variable is an element associating a name with a value. This allows you to perform operations on the variable instead of the value.
For example, we define var is a variable
var = 1
var + 1 = 2
var*5 = 10 etc.
In programming, a variable is used to store values read by the sensors and perform operations on them.
1) What are variables?

## Slide 6: I/- Variables
SESSION 2
Vriables & Loops
1)Create a variable
Verify
Name the variable

## Slide 7: I/- Variables
SESSION 2
Vriables & Loops
Try this code in micro:bit.
Can you explain the values that display on the screen of the emulator and/or robot ?
Warning : the violet block is a mathematical clock (Math section)
1) Exercise

## Slide 8: I/- Variables
SESSION 2
Vriables & Loops
Forever :
      var = 1
      Display 1 in the screen (Led matrix)
      var = 1+3 = 4
      Display 4 in the screen
      var = 4 + 4/2 = 6
      Display 6 in the screen
1) Exercise- Answer

## Slide 9: II/- Loops
SESSION 2
Vriables & Loops
Last week you learned to detect the surrounding light. For example, you want the robot to move forward only when it is light. Can you write a code to do this?
A loop is a conditional structure allowing to repeat several times the same block of instructions.
The forever block is a infinity loop. There are other types of non-infinite loops that allows to perform various operations and use sensors.
Note : Logical operators Comparators : compare 2 values, variables or data (=,>,<)
Booleans : their answer can only be "true" or "false
1) What are loops

## Slide 10: II/- Loops
SESSION 2
Vriables & Loops
The while loop executes the instructions inside the loop as long as the condition is true. Warning in this loop : the condition must be false at some point, otherwise the loop becomes infinite ! And an infinite loop can overload the computer and make it crash.
What does this program do ? What is the block that allows to leave the loop ?
2)While loop

## Slide 11: II/- Loops
SESSION 2
Vriables & Loops
2)While loop
Loop tour | Show number | Variable (var+1)
Initial | - | 0 < 5
1 | 0 | 1 < 5
2 | 1 | 2 < 5
3 | 2 | 3 < 5
4 | 3 | 4 < 5
5 | 4 | 5
End | - | -

## Slide 12: II/- Loops
SESSION 2
Vriables & Loops
The For loop executes the instructions inside the loop a defined number of times. For this, an "increment" is used which increases by 1 at each passage in the loop.
What does this program do ?
How many turns will the loop make ?
What is different from the previous program (while loop) ?
3)For loop

## Slide 13: II/- Loops
SESSION 2
Vriables & Loops
A conditional structure allows to perform an action if one or more conditions are met.
What does this program do ?
3)If-Else Structure

## Slide 14: III/- Sensors
SESSION 2
Vriables & Loops
An ultrasonic sensor can detect an obstacle, and even measure the distance to it.
The transmitter emits short, high frequency sound pulses at regular intervals. These pulses travel through the air at the speed of sound. When they hit an object, they are reflected and return as an echo to the receiver.
1) Ultrasonic sensor
Try to measure the distance and display it on the Led Matrix

## Slide 15: III/- Sensors
SESSION 2
Vriables & Loops
Line sensors detect the presence of a black line by emitting infrared (IR) light and detecting the light levels that return to the sensor. They do this using two components : an emitter and a light sensor (receiver).
Programming:
1) Line sensor

## Slide 16: IV/- The mission
SESSION 2
Vriables & Loops
RENA is now ready to leave the shuttle. Nevertheless, he needs a way to know when he will be out.
a) Write a program that displays on his screen a sun when he will be facing the daylight.
Note : use a conditional structure.
Moreover, RENA will have to avoid possible obstacles.
b) Write a program that detects obstacles and avoids them. Note : once the obstacle is detected, the robot can move backwards, turn and then move forward again.
1)Explanations

## Slide 17: IV/- The mission
SESSION 2
Vriables & Loops
That's it, your RENA leaves the space shuttle ! While leaving, RENA spots old wheel tracks corresponding to the direction followed by the last exploration mission. Help him to follow these tracks. You have at your disposal a tape allowing to draw a black line on the ground.
a) Draw a line on the ground
b) Write a program following this line
c) If you have the time, make sure that line tracking only works if it is daylight.
2)Challenge

## Slide 18: IV/- Additional time
SESSION 2
Vriables & Loops
Thanks to you, your RENA can follow the tracks of the previous mission ! Continue to expand the code by adding other modules: LEDs, Buzzer, Screen...

## Slide 19: Answers
SESSION 2
Vriables & Loops
Quiz : 1)b - 2)a - 3)b - 4)c - 5)a - 6)b
II/- Loops
2) While loop : leads to the exit of the loop 3) For loop : do exactly the same that the previous code. 5 tours (0 to 4). The bloc that allows to exit the loop in while loop is not present : the For loop does it all by itself.
4) If-Else Structure : when button A is pressed, plays a C, when button B is pressed, plays an
E. Otherwise, displays 0.
III/- Sensors
1) Ultrasonic sensor

## Slide 20: Answers
SESSION 2
Vriables & Loops
IV/- The mission
Explanations
a) warning : the number « 100 » can be modify according to light in the classroom
b) Line sensor :
Exemple Additional time :
2) Challenge :

## Slide 21
VERBANO ZUR FORDERUNG DES MINT-UNTERRICHTS
HESSEN
GYMNASIUM GOETHESCHULE
HANNOVER
- LIG.·.. U.E foRM.E·R. -IN..•FoRMER- •
TAANSF
oRMER. I
de l'enseignement